## Slide 1: Chirp rate for RCBG

## Slide 2: Bandwidth calculation

## Slide 3: Different lenses
Focal Length (mm) | Radius R (mm) | Bandwidth (nm) | Chirp Rate (nm/mm) | 
3000 | 6000 | 6.504662 | 0.260186 | 
2000 | 4000 | 9.756993 | 0.39028 | 
1500 | 3000 | 13.00932 | 0.520373 | 
1000 | 2000 | 19.51399 | 0.780559 | 
750 | 1500 | 26.01865 | 1.040746 | 
500 | 1000 | 39.02797 | 1.561119 | 
250 | 500 | 78.05595 | 3.122238 | 
100 | 200 | 195.1399 | 7.805595 | 
50 | 100 | 390.2797 | 15.61119 | 
25 | 50 | 780.5595 | 31.22238 | 

## Slide 4: How get this equation
RBG equation

## Slide 5
Chirped RBG equation
which is modulated in z
On the other hand,

## Slide 7: One plane wave and spherical waves for recording
One beam: a plane wave (i.e., infinite radius of curvature R=∞)
Other beam: a converging cylindrical wave (finite radius of curvature R)
the interference phase difference between the two beams is based on the optical path lengths. When both beams are curved, both contribute terms proportional to .
Now if one beam is a plane wave, its contribution to the phase curvature is zero.
=
So, the chirp rate would be half of the previous one.

## Slide 8: Example of recording
lambda_0= (580*1.41)= 817.8; %in nm
UV=325;%nm
L=25; %mm
f=180;%mm
Spectral bandwidth Δλ = 48.7247 nm
Chirp rate = 1.9490 nm/mm

## Slide 9: Example of recording
lambda_0= (1064*1.41); %in nm
UV=325;%nm
L=25; %mm
f=3000 (2*1500);%mm
Spectral bandwidth Δλ = 15.1513 nm
Chirp rate = 0.6061 nm/mm

## Slide 10: Recording considerations
Align the glass sample and find the zero-fringe after or before rotating glass 45 degrees.
Which glass is better? Does scattering related to the glass or setup?
Remove the piezo stage.